## Slide 1: Condition Monitoring Interval Optimisation using Failure Delay Time Concept
Darrell Leong

## Slide 2: Scope
Failure delay time concept
RTAMO’s static methodology for condition monitoring interval optimisation
Proposed dynamic methodology for condition monitoring interval optimisation
Work outstanding

## Slide 3: Failure Delay Time Concept
Failure process of asset is divided into two periods
Normal working period
  Time length from new to the point asset is first identified to be faulty
  Static condition monitoring interval optimisation
Failure delay time period
  Time length from the point asset is first identified to be faulty to failure
  If no maintenance intervention is performed
  Dynamic condition monitoring interval optimisation using incoming information
Ref: Wang, 2003; Modelling condition monitoring intervals: a hybrid of simulation and analytical approaches

## Slide 4: RTAMO: Static Interval Optimisation
3 interval optimisation schemes: reliability, availability, cost
Optimising the interval based on target reliability, R
  Inputs:
    Target reliability, R (probability asset won’t fail in any given month)
    Component failure rate, (from data base)
  Output: optimised inspection interval (T)
  Implicit equation solved numerically

## Slide 5: RTAMO: Static Interval Optimisation
3 interval optimisation schemes: reliability, availability, cost
Optimising the interval based on target availability, A
  Inputs:
    Target availability, A (proportion of time component can function)
    Component failure rate per month, (from data base)
    Downtime needed for inspection,
    Downtime needed for repair/replacement,
  Output: optimised inspection interval (T)
  Implicit equation solved numerically

## Slide 6: RTAMO: Static Interval Optimisation
Example from RTAMO verification:
  Target availability = 0.9
  Component failure rate = 0.0056
  Inspection downtime = 4 hours
  Repair downtime = 2 days
Optimised inspection interval:
38 months
Assumption: constant failure rate
  Can an ageing asset be expected to have the same constant failure rate as a newly installed asset?

## Slide 7: Failure Delay Time: Dynamic Interval Optimisation
Maintain static intervals during normal working period
Apply dynamic intervals during failure delay time period
  Starting from point where asset performance is monitored to deviate for normal working condition
  E.g. first signs of wear
Dynamic failure rate model:
  Failure rate is updated with new condition information using Bayes’ theorem
Example:
increases from 0.0056 to 0.0080
Monitoring interval reduced from 38 to 27 months

## Slide 8: Work Outstanding
Replication of RTAMO’s cost module
Review of how failure rates are dynamically updated in the failure delay time period